DIGEST Support
Document

Part 3 
The ARC System

(The Equal Arc-Second Raster Chart/Map System)

DIGEST Support Document is module-based, and is designed to provide additional information to users of DIGEST Edition 2.1 where required.

Part 3 is produced and issued under the direction of the National Imagery and Mapping Agency, Department of Defense, United States of America, on behalf of the Digital Geographic Information Working Group.

April  2001

3 The ARC System (The Equal Arc-Second Raster Chart/Map System)

3.1 Scope

3.2 References

3.3 General Description

3.3.1 The ARC System

3.3.2 Datum

3.3.3 Zones

3.3.4 Theoretical Grid System

3.3.4.1 Grid of Each Non-Polar Zone

3.3.4.2 Grid of Each Polar Zone

3.3.5 ARC Coordinates

3.3.5.1 Pixel Spacing

3.3.5.2 Possible Modification of Image Origin

3.3.6 Coordinate Conversions

3.4 ARC Coordinate Conversions

3.4.1 Notation Conventions

3.4.2 ARC System Parameters

3.4.3 Latitude and Longitude (φ84, λ84) of a Pixel at  (r, c)

3.4.3.1 Conversion of (r,c) to (φ84, λ84) in a Non-Polar Zone

3.4.3.2 Conversion of (r,c) to (φ84, λ84) in North Polar Zone

3.4.3.3 Conversion of (r,c) to (φ84, λ84) in South Polar Zone

3.4.4 Pixel Coordinates (r, c) of a Geographic Point (φ84, λ84)

3.4.4.1 Conversion of (φ84, λ84) to (r,c) in a Non-Polar Zone

3.4.4.2 Conversion of (φ84, λ84) to (r,c) in North Polar Zone

3.4.4.3 Conversion of (φ84, λ84) to (r,c) in South Polar Zone

3.4.5 Computation of Coordinates φ0 and λ0 (for Alignment of Tiling Scheme)

3.4.5.1 (φ0, λ0) within a Non-Polar Zone

3.4.5.2 (φ0, λ0) within North Polar Zone

3.4.5.3 (φ0, λ0) within South Polar Zone

3.4.6 Computation of Constants Asz and Bs

3.5  Distortion Analysis

3.5.1 North-South Distortion

3.5.2 East-West Distortion

3.1 Scope

This clause defines the Equal Arc-Second Raster Chart/Map System, more usually known as the ARC System.  The individual aspects described are:

- the geodetic datum (WGS 84);

- the 16 non-polar zones and the 2 polar zones of the system;

- the system of zone distribution rectangles (ZDRs) for raster images;

- the relative coordinate system used for pixels in the zone distribution rectangles (ARC coordinates being row & column);

- the conversion methods which relate the row & column coordinates to geographical coordinates.

3.2 References

1. Digital Geographic Information Working Group, “Digital Geographic Information Exchange Standards (DIGEST)”:

Part 1: General Description; Edition 2.1, September 2000. Part 2: Theoretical Model, Exchange Structure, and Encapsulation Rules; Edition 2.1, September 2000.

Part 3: Codes and Parameters; Edition 2.1, September 2000.
Part 4: Feature and Attribute Coding Catalogue (FACC); Edition 2.1,
September 2000.

1.	2. NIMA Technical Report 8350.2 “Department of Defense World Geodetic System 1984” (Third Edition dated 4 July 1997).

2.	3. MIL-A-89007 “ARC Digitized Raster Graphs (ADRG)”; Edition dated February 1990.

3.	4.  Snyder, John P: “Map Projections - A Working Manual” (US Geological Survey Professional Paper 1395, 1987).

3.3 General Description

3.3.1 The ARC System

The Equal Arc-Second Raster Chart/Map system, more usually known as the ARC System, is a special grid system covering the entire ellipsoid of the World Geodetic System 1984.  It provides a rectangular coordinate system based on 18 latitudinal zones.  These allow an image-dependent relative coordinate system to be used with individual raster images.  The design objective of ARC is to provide graphic data in a manner as seamless as possible, and to permit direct display with simple representation of directions.

For the purposes of this description of ARC, there is a defined region of interest called a Distribution Rectangle (DR).  More precisely, it is the minimum bounding rectangle around the raster image.  It is rectangular with respect to geographical coordinates, so it is defined by two bounding longitudes and two bounding latitudes.

3.3.2 Datum

The geodetic datum is the World Geodetic System 1984.  The constants for the WGS 84 ellipsoid (extracted from NIMA TR 8350.2) are: Semi-major axis: a = 6378137 metres (exactly) 3 − 3 Inverse flattening: Semi-minor axis: Eccentricity squared:

3.3.3 Zones

1/f = 298.257223563 (now a defining parameter) b = 6356752.3142 metres (derived from 1/f and a) e2 = 0.00669437999013 (derived from 1/f)

The basic zones, in the sense of the zones exclusive of overlaps, are defined in Table 3-1 and illustrated in Figures 3-1 and 3-2.

Table 3-1 ARC Zones

| Northern Zones | Latitude Range | Southern Zones | Latitude Range |
| --- | --- | --- | --- |
| Zone 1 | 0°N to 32°N | Zone 10 | 0°S to 32S° |
| Zone 2 | 32°N to 48°N | Zone 11 | 32°S to 48S° |
| Zone 3 | 48°N to 56°N | Zone 12 | 48°S to 56S° |
| Zone 4 | 56°N to 64°N | Zone 13 | 56°S to 64S° |
| Zone 5 | 64°N to 68°N | Zone 14 | 64°S to 68S° |
| Zone 6 | 68°N to 72°N | Zone 15 | 68°S to 72S° |
| Zone 7 | 72°N to 76°N | Zone 16 | 72°S to 76S° |
| Zone 8 | 76°N to 80°N | Zone 17 | 76°S to 80S° |
| Zone 9 (Polar) | 80°N to 90°N | Zone 18 (Polar) | 80°S to 90S° |

Notes: 1. These ranges are exclusive of overlaps.

2. All zones include the full longitude range.

| ↑Latitude (φ) |
| --- |
| 80°N | Zone 8 |
| 76°N | Zone 7 |
| 72°N | Zone 6 |
| 68°N | Zone 5 |
| 64°N | Zone 4 |
| 56°N | Zone 3 |
| 48°N |  |
|  | Zone 2 |
| 32°N |  |
| 180°W |  | Zone 1 | 180°E |
|  |  |  | Longitude |
|  |  |  | (λ) → |
|  | 0°N |  |  |
|  |  | Zone 10 |  |
|  | 32°S |  |  |
|  |  | Zone 11 |  |
|  | 48°S |  |  |
|  |  | Zone 12 |  |
|  | 56°S |  |  |
|  |  | Zone 13 |  |
|  | 64°S | Zone 14 |  |
|  | 68°S | Zone 15 |  |
|  | 72°S | Zone 16 |  |
|  | 76°S | Zone 17 |  |
|  | 80°S |  |  |
|  |  | 0°E |  |

This illustrates the relative size of non-polar zones, each of which represents the range 180°W to 180°E.

Figure 3-1.  ARC System Non-Polar Zones 180°W0°E

0°E 180°W Zone 9: North Polar Zone Zone 18: South Polar Zone

Area around the defining circles is only used for padding raster images.

Figure 3-2.  ARC System Polar Zones

For raster images based on the ARC System, each non-polar zone is considered to have a Zone Overlap.  This is the overlap into the next zone poleward by 1024 rows of pixels, thus duplicating coverage of 1024 rows of the next zone.  The precise north-south distance covered by the overlap depends on the scale of data portrayed in that zone.

At latitudes defined by the ARC system zone limits, the raster data for a DR is divided into images called Zone Distribution Rectangles (ZDRs).  There is one ZDR for each ARC system zone (including the overlap) covering any part of the DR; the ZDR depicts all the DR data that falls within that zone's limits. A DR covered by only one zone will thus contain a single ZDR; a DR covered by more than one zone will contain more than one ZDR.  Note that a DR which is fully covered by one zone but which lies at the equatorward limit of that zone is also covered by the overlap portion of the adjoining equatorward zone and will contain 2 ZDRs (one depicting the entire DR and a second depicting that part of the DR covered by the adjoining zone's overlap).

Another concept related to ARC zones is the Standard Latitude.  It is best understood as the latitude chosen for distortion-free representation of east-west scale.  The circumference of the standard latitude in a non-polar zone is treated as the length of the band representing that zone.

3.3.4 Theoretical Grid System

The grid of each ARC zone is theoretical, in the sense that the zone eastings and northings are not the same as ARC coordinates. ARC coordinates are actually relative coordinates, referenced to the ZDR, scaled from the zone eastings and northings.

3.3.4.1 Grid Of Each Non-Polar Zone

The projection used is the Equirectangular projection described in Snyder, Pages 90-91. The formulae are

x = (R cos φstd) λ and y = R φ ,

where φ and λ are in radians, R is the radius of the approximating sphere and φstd is the standard latitude.

The standard latitude is an intermediate latitude between the two limits, defined in such a way as to make the maximum stretch equivalent to the maximum shrink.  The precise definition is given in 3.5.  Table 3-2 gives the values for each zone.

Table 3-2 Standard Latitudes Of The ARC Non-Polar  Zones

| Northern Zones | Standard Latitude | Southern Zones | Standard Latitude |
| --- | --- | --- | --- |
| Zone 1 | 22.94791772°N | Zone 10 | 22.94791772S° |
| Zone 2 | 41.12682127°N | Zone 11 | 41.12682127S° |
| Zone 3 | 52.28859923°N | Zone 12 | 52.28859923S° |
| Zone 4 | 60.32378942°N | Zone 13 | 60.32378942S° |
| Zone 5 | 66.09421768°N | Zone 14 | 66.09421768S° |
| Zone 6 | 70.10896259°N | Zone 15 | 70.10896259S° |
| Zone 7 | 74.13230145°N | Zone 16 | 74.13230145S° |
| Zone 8 | 78.17283750°N | Zone 17 | 78.17283750S° |

Although the maximum distortion in each zone (without overlap) is minimised, it is still very large in comparison to most grid systems.  In zone 2, for example, there is a 1→1.1253 stretch along the Pole-ward latitude and a 1.1253→1 (or 1→0.8887) shrink along the Equatorward latitude. The distortion, which can be up to 18% between the formal latitude limits can rise to 25% in the overlap, although this depends on the size of the overlap and how near it is to the pole.

The absolute coordinates (x, y) on the theoretical grid are not used in practice, because it is relatively easy to convert directly between WGS 84 geographical coordinates (φ, λ) and ARC coordinates (r, c): r is a linear function of φ, and c is a linear function of λ. Figure 3-1 therefore omits the X axis (which would be the line representing the Equator) and the Y axis (which would be the line representing the zero meridian).

3.3.4.2 Grid Of Each Polar Zone

The projection used is the Azimuthal Equidistant projection, polar aspect, spherical form, described in Snyder, Pages 191-195.  Its simplicity is best understood by looking at Figure 3-2 and imagining each 80° polar cap represented as a flat circle with each degree of latitude treated as one tenth of the radius.  (Each arc-second of latitude is represented as 1/36000 of the radius.)

Given that the ARC System applies the projection with zero as the central longitude, the X and Y axes are as shown in Figure 3-2.  The projection formulae are

x = (R sin λ) (π/2 -φ) and y = (-R cos λ) (π/2 -φ)

in the north polar aspect, and

x = (R sin λ) (π/2 + φ) and y = (R cos λ) (π/2 + φ)

in the south polar aspect.  In each case, φ and λ are in radians, while R is the radius of the approximating sphere.  ARC uses the semi-major axis 6378137m as R.

The absolute coordinates (x, y) on the theoretical grid are only used as intermediate values when converting between WGS 84 geographical coordinates (φ, λ) and ARC coordinates (r, c).

Distortion is considerably less than in the non-polar zones.  Both east-west and north-south distortion are less than 1%, and the same is true of one relative to the other.

3.3.5 ARC Coordinates

ARC coordinates (r, c) specify the row and column of a pixel in a ZDR.  For that reason, they are also known as ZDR coordinates.  The top left pixel has ZDR coordinates (0, 0) and the position of its top-left corner is denoted (φ0, λ0) in WGS 84 coordinates.  See Figure 3-3.

Figure 3-3.  ARC Coordinates Within A ZDR

3.3.5.1 Pixel Spacing

Since r and c are the number of pixels from the top-left corner to a given position, their value depends on the size of the pixel.

The constant Bs is used to denote the number of pixels per 360° of latitude. Fixing that number is equivalent to fixing the height of a pixel.  Its value depends on the scale used for the raster image, hence the subscript s, although it must be a multiple of 512.  The precise relationship is given in 3.4.6, but is best illustrated by Table 3-3.

Table 3-3 Examples of North-South Pixel Spacing Constants

| Scale→ | 1:1 000 000 | 1:500 000 | 1:250 000 | 1:100 000 | 1:50 000 |
| --- | --- | --- | --- | --- | --- |
| Bs in any zone | 400 384 | 800 768 | 1 601 536 | 4 003 840 | 8 007 680 |

In the non-polar zones, the constant Asz is used to denote the number of pixels needed go round the parallel of standard latitude, ie the number of pixels per 360° of longitude.  Fixing that number is equivalent to fixing the width of a pixel.  Its value depends not only on scale but on the zone; this because the parallels are shorter in the zones nearer the poles.  Again, it must be a multiple of 512. The precise relationship is given in 3.4.6, but is best illustrated by the following examples:

Table 3-4 Examples of East-West Pixel Spacing Constants

| Scale→ | 1:1 000 000 | 1:500 000 | 1:250 000 | 1:100 000 | 1:50 000 |
| --- | --- | --- | --- | --- | --- |
| Asz in zones 1, 10 | 369 664 | 739 328 | 1 478 656 | 3 696 640 | 7 393 280 |
| Asz in zones 2, 11 | 302 592 | 615 184 | 1 210 368 | 3 025 920 | 6 151 840 |
| Asz in zones 3, 12 | 245 760 | 491 520 | 983 040 | 2 457 600 | 4 915 200 |
| Asz in zones 4, 13 | 199 168 | 398 336 | 796 672 | 1 991 680 | 3 983 360 |
| Asz in zones 5, 14 | 163 328 | 326 656 | 653 312 | 1 633 280 | 3 266 560 |
| Asz in zones 6, 15 | 137 216 | 274 432 | 548 864 | 1 372 160 | 2 744 320 |
| Asz in zones 7, 16 | 110 080 | 220 160 | 440 320 | 1 100 800 | 2 201 600 |
| Asz in zones 8, 17 | 82 432 | 164 864 | 329 728 | 824 320 | 1 648 640 |

In the polar zones, only the constant Bs is really needed.  However, to preserve the association of Asz and Bs with pixel-width and pixel-height respectively, it is convenient to specify that

Asz (in the polar case) is the number of pixels needed to go round the 90°N-90°S meridian circumference (making it the pixel-spacing constant along the X axis), and

Bs is the number of pixels needed to go round the 0°N-180°N meridian circumference (making it the pixel-spacing constant along the Y axis).

In polar zones, Asz is always equal to Bs, and Bs has already been tabulated for all zones.

3.3.5.2 Possible Modification Of Image Origin

When using the ARC System, there may be a requirement to have the point (φ0, λ0) an exact number of tiles from the zero meridian and the Equator.  The tile could, for instance, be 128 by 128 pixels.  An algorithm for obtaining such a point (φ0, λ0) from an original upper-left corner (φUL, λUL) is given in 3.4.5.

3.3.6 Coordinate Relationships

The relationship between the WGS 84 geographical coordinates (φ, λ) and the ARC coordinates (r, c) depend on:

the position (φ0, λ0) of the top-left corner of the ZDR, and

the pixel-spacing constants Asz and Bs, which in turn depend on scale and zone.

The formulae are given in 3.4.3 and 3.4.4.  In the non-polar zones, r is a rounded negative multiple of  (φ -φ0) while c is a rounded positive multiple of (λ -λ0). In the polar zones, it is easier to relate (φ, λ) to the absolute grid coordinates (x, y).

3.4 ARC Coordinate Conversions

This sub-clause is not essential for a general understanding of the ARC System.  However, it is normative in the sense of describing the formulae needed for implementation.

3.4.1 Notation Conventions

Throughout sub-clause 3.4, round ( ) denotes "nearest integer to".

Throughout sub-clause 3.4, φ84 denotes latitude with respect to WGS 84 and λ84 denotes longitude with respect to WGS 84.  (The subscripts are not strictly necessary in a paper describing the relationship between ARC coordinates and WGS 84 coordinates. However, the subscripts help to avoid ambiguity, particularly if the information is applied to a raster specification where a datum of a source graphic is involved as well as the WGS 84 datum.)

3.4.2 ARC System Parameters

| Parameter | Description | Tags |
| --- | --- | --- |
| (φ0, λ0) | WGS 84 coordinates of the Zone Distribution Rectangle | PSO, LSO |
|  | (ZDR) (0, 0) pixel |  |
| Asz | East-West pixel spacing at scale 1:S in zone Z | ARV |
| Bs | North-South pixel spacing at scale 1:S | BRV |

where units for latitude and longitude are decimal degrees.

Note that other parameters would be needed if the datum of the source graphic is involved in the raster application.

3.4.3 Latitude and Longitude (φ84, λ84) of a Pixel at (r, c)

| Parameters Used: |
| --- |
| Parameter | Description | Tag |
| (φ0, λ0) | WGS 84 coordinates of the ZDR (0, 0) pixel | PSO, LSO |
| Asz | East-West pixel spacing at scale 1:S in zone Z | ARV |
| Bs | North-South pixel spacing at scale 1:S | BRV |
| 3.4.3.1 | Conversion of (r,c) to (φ84, λ84) in a Non-Polar Zone |  |
| φ84 = φ0 -(360°r/Bs) |  |
| λ84 = λ0 + (360°c/Asz) |  |
| 3.4.3.2 | Conversion of (r,c) to (φ84, λ84) in North Polar Zone |  |

(1) ARC System Coordinates  (x0, y0) at (φ0, λ0)

x0 = (Bs/360°) (90° -φ0) sin(λ0)
y0 = - (Bs/360°) (90° -φ0) cos(λ0)

(2)	ARC System Coordinates  (x, y) at (r, c) x = x + c

0

y = y0 -r

| (3) WGS 84 Coordinates (φ84, λ84) at (x, y) |
| --- |
| φ84 | = | 90° | -[(x2 + y2)1/2 / (Bs/360°)] |
| λ84 | = | arccos[-y/(x2 + y2)1/2 ] | if | x | > 0 or | x | = | 0, y ≠ 0 |
| λ84 | = | - arccos[-y/(x2 + y2)1/2 ] | if | x | < 0 |  |  |
| λ84 | = | 0° | (i.e., undefined) | if | x | = | y | = | 0 |
| where 0° <= arccos[-y/(x2 + y2)1/2 ] <= 180° |  |  |  |

3.4.3.3 Conversion of (r,c) to (φ84, λ84) in South Polar Zone

(1) ARC System Coordinates  (x0, y0) at (φ0, λ0)

x0 = (Bs/360°) (90° + φ0) sin(λ0)
y0 = (Bs/360°) (90° + φ0) cos(λ0)

.	(2)	ARC System Coordinates  (x, y) at (r, c) x = x + c

0

y = y0 -r

| (3) WGS 84 Coordinates (φ84, λ84) at (x, y) |
| --- |
| φ84 | = | -90° + [(x2 + y2)1/2 / (Bs/360°)] |
| λ84 | = | arccos[y/(x2 + y2)1/2 ] | if | x | > 0 or | x | = | 0, y ≠ 0 |
| λ84 | = | - arccos[y/(x2 + y2)1/2 ] | if | x | < 0 |  |  |
| λ84 | = | 0° | (i.e., undefined) | if | x | = | y | = | 0 |
| where 0° <= arccos[y/(x2 + y2)1/2 ] <= 180° |  |  |  |

3.4.4 ZDR Pixel Coordinates (r, c) of a Geographic Point  (φ84, λ84)

| Parameters Used: |
| --- |
| Parameter | Description | Tag |
| (φ0, λ0) | WGS 84 coordinates of the ZDR (0, 0) pixel | PSO, LSO |
| Asz | East-West pixel spacing at scale 1:S in zone Z | ARV |
| Bs | North-South pixel spacing at scale 1:S | BRV |

3.4.4.1 Conversion of (φ84, λ84) to (r,c) in a Non-Polar Zone

r = round [(φ0 -φ84) (Bs/360°)] c = round [(abs (λ84 -λ0) mod 360°) (Asz/360°)]

3.4.4.2 Conversion of (φ84, λ84) to (r,c) in North Polar Zone

.	(1) ARC System Coordinates  (x0, y0) at (φ0, λ0)

.	x0 = (Bs/360°) (90° -φ0) sin(λ0) y0 = - (Bs/360°) (90° -φ0) cos(λ0)

.	(2) ARC System Coordinates  (x, y) at (φ84, λ84)

.	x = (Bs/360°) (90° -φ84) sin(λ84) y = - (Bs/360°) (90° -φ84) cos(λ84)

.	(3) ZDR Pixel Coordinates  (r, c) at (x, y)

r = round (y0 - y) c = round (x - x0)

3.4.4.3 Conversion of (φ84, λ84) to (r,c) in South Polar Zone

.	(1) ARC System Coordinates  (x0, y0) at (φ0, λ0)

.	x0 = (Bs/360°) (90° + φ0) sin(λ0)
y0 = (Bs/360°) (90° + φ0) cos(λ0)

.	(2) ARC System Coordinates  (x, y) at (φ84, λ84)

.	x = (Bs/360°) (90° + φ84) sin(λ84)
y = (Bs/360°) (90° + φ84) cos(λ84)

.	(3) ZDR Pixel Coordinates  (r, c) at (x, y)

r = round (y0 - y)
c = round (x - x0)

3.4.5 Computation of Coordinates φ0 and λ0 (For Alignment of Tiling Scheme)

This algorithm is applicable when there is a requirement to have the point (φ0, λ0) an exact number of  tiles from the zero meridian and the Equator, given a tile-size of 128×128 pixels.

| Parameters Used: |
| --- |
| Parameter | Description | Tag |
| Asz | East-West pixel spacing at scale 1:S in zone Z | ARV |

Bs North-South pixel spacing at scale 1:S BRV

The coordinates of the image origin (φ0, λ0) depend on the pixel spacing constants adjusted for the scale and zone of the image data.

The width of the pixel is 360°/Asz and in the E-W direction and 360°/Bs in the N-S direction. For polar zones, Asz = Bs.

Let (φUL, λUL) denote the WGS 84 coordinates of the upper left point of the image. For nonpolar zones, φUL is the northernmost latitude and λUL is the westernmost longitude.

3.4.5.1 (φ0, λ0) within a Non-Polar Zone

Let Δφ and Δλ denote the length of a tile of 128 by 128 pixels.

Δφ = 46080°/Bs
Δλ = 46080°/Asz

φ0 is φUL rounded up to the next integral multiple of Δφ (to ensure an exact number of tiles to the Equator). Equivalently, φ0 is n(Δφ) where n is φUL /Δφ  rounded up to an integer.

λ0 is λUL rounded down to the next integral multiple of Δλ (to ensure an exact number of tiles to the Prime Meridian).  Equivalently, λ0 is n(Δλ) where n is λUL /Δλ rounded down to an integer.

3.4.5.2 (φ0, λ0) within North Polar Zone DIGEST Support Document

| x0 | = | (Bs/360°) (90° -φUL) sin(λUL) | rounded down to the next multiple of 128. |
| --- | --- | --- | --- |
| y0 | = | - (Bs/360°) (90° -φUL) cos(λUL) | rounded up to the next multiple of 128. |
| φ0 | = | 90° | -[(x0 2 + y0 2)1/2 (360°/Bs)] |  |
| λ0 | = | arccos[-y0/(x0 2 + y0 2)1/2 ] | if | x0 | > 0 or | x0 | = | 0, y0 | ≠ 0 |
| λ0 | = | - arccos[-y0/(x0 2 + y0 2)1/2 ] | if | x0 | < 0 |
| λ0 | = | 0° | if | x0 | = | y0 | = | 0 |
| where the range of arccos is 0° to 180°. |  |
| 3.4.5.3 | (φ0, λ0) within South Polar Zone |  |
|  | x0 | = | (Bs/360°) (90° + φUL) sin(λUL) | rounded down to the next multiple of 128. |
|  | y0 | = | (Bs/360°) (90° + φUL) cos(λUL) | rounded up to the next multiple of 128. |
|  | φ0 | = | -90° + [(x0 2 + y0 2)1/2 (360°/Bs)] |  |
|  | λ0 | = | arccos[y0/(x0 2 + y0 2)1/2 ] | if | x0 | > 0 or | x0 | = | 0, y0 | ≠ 0 |
|  | λ0 | = | - arccos[y0/(x0 2 + y0 2)1/2 ] | if | x0 | < 0 |
|  | λ0 | = | 0° | if | x0 | = | y0 | = | 0 |
|  | where the range of arccos is 0° to 180°. |  |

3.4.6 Computation of Constants Asz and Bs

Pixel spacing constants and spacing intervals for all zones at the scale 1:1,000,000 are shown in Table 3-5 below. Table 3-5 Pixel Spacing Constants A and B Zone Limits 1 Nominal Pixel Spacing 2

| Zone | Equator | Pole |  |  | Longitude | Latitude |
| --- | --- | --- | --- | --- | --- | --- |
| Number | -ward | -ward | A | B | (microns) | (microns) |
| 1, 10 | 0 | 32 | 369664 | 400384 | 99.9 | 99.9 |
| 2, 11 | 32 | 48 | 302592 | 400384 | 99.9 | 99.9 |
| 3, 12 | 48 | 56 | 245760 | 400384 | 100.0 | 99.9 |
| 4, 13 | 56 | 64 | 199168 | 400384 | 99.9 | 99.9 |
| 5, 14 | 64 | 68 | 163328 | 400384 | 99.7 | 99.9 |
| 6, 15 | 68 | 72 | 137216 | 400384 | 99.7 | 99.9 |
| 7, 16 | 72 | 76 | 110080 | 400384 | 99.8 | 99.9 |
| 8,17 | 76 | 80 | 82432 | 400384 | 100.0 | 99.9 |
| 9,18 | 80 | 90 | 400384 | 400384 | 99.9 | 99.9 |

NOTES: 1. Latitudes are shown unsigned for convenience.

2.	Measured at the latitude which gives equivalent stretch and shrink at zone limits on the WGS 84 ellipsoid.

To compute the pixel spacing constants for a graphic at scale 1:S in zone Z (i.e., Asz and Bs), first compute the real scale factor N using the following equation:

N = 	1,000,000 / S

The A and B values for 1:1,000,000 are multiplied by N and the results rounded up to the next multiple of 512 to give the values Asz and Bs.

NOTE: The A and B values provided with the image data may already be adjusted for the scale and zone of the image data.

3.5 	Distortion Analysis

Distortion in the ARC System is significant in the non-polar zones, where it is almost entirely due to distortion in the east-west directions. Distortion can be quantified in terms of the latitude, the ellipsoidal constant e2, and (in the east-west case) the zone.

3.5.1 North-South Distortion

As shown in Table 3-6, distortion in the north-south directions is small in all zones.  The effect of treating meridians as circles with a 6378137m radius is to treat 1″ of latitude as 30.9221m. This is only a 0.34% shrink of the true value at the poles (31.0261m) and only a 0.67% stretch of the true value at the Equator (30.7151m). The north-south distortion ratio (projected distance divided by ellipsoidal distance) at latitude φ is

(1 - e2sin2φ)3/2 / (1 - e2).

Table 3-6  North-South Distortion at Zone-Limit Latitudes

| Latitude (unsigned) | N-S Distortion Factor | Shrink (%) | Latitude (unsigned) | N-S Distortion Factor | Stretch (%) |
| --- | --- | --- | --- | --- | --- |
| 90° | 0.996647 | 0.34 | 48° | 1.001162 | 0.12 |
| 80° | 0.996951 | 0.30 | 32° | 1.003902 | 0.39 |
| 76° | 0.997237 | 0.28 | 0° | 1.006739 | 0.67 |
| 72° | 0.997609 | 0.24 |  |  |  |
| 68° | 0.998061 | 0.19 |  |  |  |
| 64° | 0.998584 | 0.14 |  |  |  |
| 56° | 0.999799 | 0.02 |  |  |  |

3.5.2 East-West Distortion

East-West distortion is so much greater than north-south distortion (except in the polar zones where both are small) that it is usual to quantify distortion purely in terms of the east-west direction. The maximum stretch and shrink for each zone is shown in Table 3-7 below. Also indicated is the standard latitude at which nominal pixel spacing is defined.  These values apply for all scales of data.

Table 3-7 Standard Latitudes and Maximum Distortion (Exclusive of Overlap)

| Zone |  | Latitude (degrees) |  | Distortion |
| --- | --- | --- | --- | --- |
|  | Equatorward | Standard (zero distortion) | Poleward | Maximum Stretch (%) | Maximum Shrink (%) |
| 1, 10 | 0 | 22.94791772 | 32 | 8.54 | 7.87 |
| 2, 11 | 32 | 41.12682127 | 48 | 12.53 | 11.13 |
| 3, 12 | 48 | 52.28859923 | 56 | 9.36 | 8.56 |
| 4, 13 | 56 | 60.32378942 | 64 | 12.92 | 11.44 |
| 5, 14 | 64 | 66.09421768 | 68 | 8.17 | 7.55 |
| 6, 15 | 68 | 70.10896259 | 72 | 10.09 | 9.17 |
| 7, 16 | 72 | 74.13230145 | 76 | 13.01 | 11.51 |
| 8, 17 | 76 | 78.17283750 | 80 | 18.03 | 15.27 |
| 9, 18 | 80 | 81.94975621 | 90 | 0.18 | 0.34 |

The mathematics of the east-west distortion is given below.

(1) In the non-polar zones, to minimise the maximum distortion in the zone, the standard latitude φstd is chosen such that its circumference is the geometric mean of the two bounding circumferences of the zone.  Equivalently, φstd is the value of φ for which

log cos φ -0.5log(1 - e2sin2φ) is halfway between its values at the bounding latitudes.  The east-west distortion ratio (projected distance divided by ellipsoidal distance) at latitude φ is

[cos φ √(1 - e2sin2φstd)]/[ cos φstd √(1 - e2sin2φ)]. This formula can be used to compute the east-west distortion in the overlap of a non-polar zone.

(2) In the polar zones, the standard latitude is not a defining parameter of the projection, but exists in the sense that there is a latitude of zero distortion.  The east-west distortion ratio (projected distance divided by ellipsoidal distance) at latitude φ is

(θ/sinθ)√(1 - e2sin2φ),

where θ is the difference in radians between φ and the latitude of the pole. The standard latitude is the latitude where that ratio equals 1, and that latitude is 81.94975621°.