DIGEST Support
Document

Part 2 Table of Options for Encoding
Geographic Entities

DIGEST Support Document is module-based, and is designed to provide additional information to users of DIGEST Edition 2.0 where required.

Part 2 is produced and issued under the direction of the Centro Informazioni Geotopografiche Aeronautiche (CIGA), IT, on behalf of the Digital Geographic Information Working Group.

June 1997

5.1 Use of FACC

FACC has not been developed to the requirements of any single application, or level of resolution, and in itself cannot support a digital product. For a product, the menus of features and attributes must be employed in concert with a product specification. Users of FACC re advised that, as with any dictionary, there may be more than one way to encode geographic entities, either by offering a choice of features or a combination of features and attributes. For example, a heliport is listed as feature GB035 (Heliport), but could also been coded as feature code GB006 (Airfield) with attribute APT (Airfield type) with a coded value of 009 (Heliport). Another example would be AK090 (Fairgrounds) and AK091 (Exhibition Grounds) which could be interchanged, depending on the user's own interpretation. This table should be useful to the product developer who can tailor the coding to best fit the application.

If a geographic feature does not reside within FACC, DIGEST allows for a Data Dictionary to store user-designated features and associated attributes. Otherwise, features and attributes shall be encoded using the FACC standard. The procedure for amending and updating FACC is described in Section 5.3.

Table of Options for Encoding Geographic Entities

A listing of features, attributes and attribute values that allows both product and system designers to examine alternative ways to encode the same or similar geographical entities. It should be noted that the selection of the appropriate code or combination of codes is highly dependent upon the context in which it is to be used. This list, the result of a thorough review of FACC by subject matter experts, does not claim to represent every conceivable way to encode geographic entities.

| Geographic Entity (Feature Name) | Feature Code | Attribute Code | Alternative Feature Code(s) | Alternative Feature + Attribute Code(s) |
| --- | --- | --- | --- | --- |
| Amusement Park | AK030 |  | AK090 Fairgrounds AK091 Exhibition Grounds |  |
| Anchor Berth | BB012 | MAC012 |  | FC031 Maritime Area + MAC012 Anchorage Berths |
| Anchorage | BB010 | MAC011 |  | FC031 Maritime Area + MAC011 Anchorage (general) |
| Anchorage | BB011 | MAC011 |  | FC031 Maritime Area + MAC011 Anchorage (general) |

| Geographic Entity (Feature Name) | Feature Code | Attribute Code | Alternative Feature Code(s) | Alternative Feature + Attribute Code(s) |
| --- | --- | --- | --- | --- |
| Benchmark | ZB020 | CPA011 |  | ZB035 Control Point / Control Station + CPA011 Benchmark |
| Bog | BH015 |  |  | DA010 Ground Surface Element + STP015 Peat DA010 Ground Surface Element + VEG007 Peat |
| Bollard | BB030 | MWF004 |  | BB079 Mooring/Warping Facility + MWF004 Bollard |
| Bridge Tower/Bridge Pylon | AQ055 |  |  | AL240 Tower (Non-Communication) + TTC001 Bridge |
| Building | AL015 |  | AL100 Hut |  |
| Causeway | AQ064 |  |  | AP030 Road + USE127 as a Causeway |
| Cleared Way/Cut Line/Firebreak | EC040 | USE122 |  | EC015 Forest + VEG052 Forest Clearing EC015 Forest + USE122 Firebreak |
| Common Open Water | SA010 |  | BA040 Water (Except Inland) | BH000 Inland Water |
| Communication Building | AT050 |  |  | AT015 Building + USE134 Utilities and Transportation |
| Control Tower | AQ060 |  |  | AL240 Tower (Non-Communication) + TTC016 Control AT080 Communication Tower + TTC016 Control |
| Dam/Weir | BI020 |  | BI043 Flood Barrage |  |

| Geographic Entity (Feature Name) | Feature Code | Attribute Code | Alternative Feature Code(s) | Alternative Feature + Attribute Code(s) |
| --- | --- | --- | --- | --- |
| Deep Water Route | FC166 | RTT004 |  | FC165 Route (Maritime) + RTT004 Deep Water Route + RTT098 Deep Water Route-Centerline + RTT099 Deep Water Route-Part |
| Depression | DB080 | COT001 |  | CA010 Contour Line (Land) + COT001 Depression |
| Dolphin | BB080 | MWF002 |  | BB079 Mooring/Warping Facility + MWF002 Dolphin |
| Dragon Teeth | AL060 | SSC081 |  | AP041 Barrier +SSC081 Dragons Teeth |
| Exposed Bedrock | SA030 |  |  | DA010 Ground Surface Element + SMC007 Bedrock |
| Fish Stakes | BB100 | FFC001 |  | FC031 Maritime Area + FFC001 Fishing Stake |
| Fish Traps/Fish Weirs | BB110 | FFC002 FFC003 |  | FC031 Maritime Area + FFC002 Fish trap + FFC003 Fish weirs + MAC056 Fish Trap Area |
| Fog Signal | BC101 | STA022 |  | BC010 Beacon + LFA056 Fog Detector + LFC007 Fog Detector Light + SST003 Explosive Fog Signal + SST008 Radio Fog Signal + SST010 Submarine Fog Bell + STA022 Fog Signal |
| Forest | EC015 |  | EC030 Trees |  |

| Geographic Entity (Feature Name) | Feature Code | Attribute Code | Alternative Feature Code(s) | Alternative Feature + Attribute Code(s) |
| --- | --- | --- | --- | --- |
| Fountain | BH075 |  |  | AA050 Well + WFT004 Fountain |
| Geothermal Feature | DB115 |  |  | BH170 Spring/Water-Hole + SWT001 Geyser + SWT002 Hot Spring + SWT003 Fumarole |
| Highway Sign |  | USE019 |  | AL050 Display Sign + USE019 Highway Sign AL080 Gantry + USE019 Highway Sign |
| Interchange | AP020 |  | AQ062 Crossing |  |
| Jetty | BB140 |  | BB040 Breakwater/Groyne |  |
| Leading Light(s) | BC030 | LFC004 |  | BC040 Light + LFC004 Leading Light |
| Lighthouse | BC050 | BFC082 |  | AL015 Building + BFC082 Lighthouse |
| Measured Distance Line | FC100 | RTT007 |  | FC165 Route (Maritime) + RTT007 Measured Distance Line |
| Mole | BB042 |  | BB190 Pier/Wharf/Quay |  |
| Native Settlement | AL135 | PPT002 |  | AL020 Built-Up Area + PPT002 Native Settlement |
| Oil/Gas Facilities | AC040 |  |  | AL020 Built-Up Area + AFA009 Fuel Station + AFA011 Bottle Gas/LPG |
| Permanent Snowfield | SA040 |  | BJ100 Snow Field/Ice Field |  |
| Picnic Site | AK061 |  | AK120 Park |  |

| Geographic Entity (Feature Name) | Feature Code | Attribute Code | Alternative Feature Code(s) | Alternative Feature + Attribute Code(s) |
| --- | --- | --- | --- | --- |
| Platform | BD110 |  | BD111 Offshore Platform Site |  |
| Polar Ice | BJ080 | ICC008 |  | BJ100 Snow field/Ice Field + IC008 Polar Ice |
| Potential Landslide Area | DB210 | SRD002 |  | DA010 Ground Surface Element + SRD002 Area of high landslide potential DB160 Rock Strata/Rock Formation + SRD002 Area of high landslide potential |
| US-Power Plant UK-Power Generation | AD010 | BFC083 |  | AL015 Building + BFC083 Power Generation |
| Processing Plant/Treatment Plant | AC000 |  |  | AL015 Building + BFC089 Processing/Treatment |
| Ramp | BB020 |  | BB240 Slipway/Patent Slip |  |
| Reservoir | BH130 | POP002 |  | BH080 Lake/Pond + POP002 Reservoir |
| Restricted Area | FC036 | MAC007 |  | FC031 Maritime Area + MAC007 Restricted Area |
| Rock Strata/Rock Formation | DB160 |  |  | DA010 Ground Surface Element + SMC007 Bedrock + SMC084 Rock/Rocky |
| Safety Fairway | FC170 | RTT008 |  | FC165 Route (Maritime) + RTT008 Safety Fairway/Channel |
| Salt Evaporator | BH155 | SRD087 |  | DA010 Ground Surface Element + SRD087 Salt Evaporators |
| Sand Dune/Sand Hills | DB170 | SRD038 |  | DA010 Ground Surface Element + SRD038 Sand Dunes |

| Geographic Entity (Feature Name) | Feature Code | Attribute Code | Alternative Feature Code(s) | Alternative Feature + Attribute Code(s) |
| --- | --- | --- | --- | --- |
| School |  | BFC015 |  | AL015 Building + USE901 School |
| Seaplane Base | GB065 | APT004 |  | GB005 Airport/Airfield + APT004 Seaplane Base |
| Shed | AL019 | BFC098 |  | AL015 Building + BFC098 Shed |
| Snow Shed/Rock Shed | AL210 | USE115 USE116 |  | AL075 Gallery + USE115 Snow Shed + USE116 Rock Shed |
| Swept Area | FC177 | MAC010 |  | FC031 Maritime Area + MAC010 Wire Drag Area/Swept Area |
| Telephone-Telegraph Pylon/Pole | AT070 |  |  | AQ021 Mast + USE134 Utilities and Transportation |
| Tower | AL241 |  |  | AL240 Tower (Non-Communication) + TTC000 Unknown AL240 Tower (Non-Communication) + TTC004 Undefined |
| Tunny (Tuna) Nets Area | BB111 | FFC004 |  | FC031 Maritime Area + FFC004 Tunny/Tuna Net |
| Underground Danger/Hazard | BD000 |  | BD070 Obstruction (Nautical) |  |
| Underground Danger/Hazard | BD000 |  |  | BD005 Miscellaneous Underwater Feature + SOH001 Dangerous |
| Water Tower | AM080 | TTC006 |  | AL240 Tower (Non-Communication) + TTC006 Water Tower |

| Geographic Entity (Feature Name) | Feature Code | Attribute Code | Alternative Feature Code(s) | Alternative Feature + Attribute Code(s) |
| --- | --- | --- | --- | --- |
| Well + LOC004 Below Surface/Submerged + SOH001 Dangerous | AA050 |  |  | BD000 Underwater Danger/Hazard + SFC004 Well |
| Wreck + LOC004 Below Surface/Submerged + SOH001 Dangerous | BD180 |  |  | BD000 Underwater Danger/Hazard + WRK002 Dangerous Wreck |
| Wreck | BD180 |  |  | BD180 Underwater Danger + WRK004 Wreck showing mast |